## Slide 1: Towards a Better Understanding Of the TEK-Vario Part III

## Slide 2: 10.1 FAQs: Why are there so many different probes?
Prandtl probe
ambient pressure
(Epot)
(-Ekin)
Braunschweiger probe
total pressure (Epot + Ekin)
The front hole of the Prandtl probe
measures total pressure.
Its side holes take ambient pressure.
And the Braunschweiger probe delivers
-Ekin. All in all, these are the data the
TEK-Vario needs to do its job properly.

## Slide 3: 10.2 FAQs: How do I get maximum performance out of my TEK-Vario-equipped model?
Based on his experience and physical knowledge, Philip recommends to proceed as follows:
Step 1 Flight Modes
Use flight modes when setting up your glider.
Start/climb, gliding, thermal 1 and 2 and landing is an appropriate set
of flight modes to start with. Always allow for a transition delay of about
1 to 2 seconds when switching from one flight mode to another.
Step 2 Trimming
After trimming your control surfaces within a flight mode, always
consider the newly adjusted position as “neutral“ or “0“.

## Slide 4: 10.2 FAQs: How do I get maximum performance out of my TEK-Vario-equipped model? (Cont´d)
Step 3 Maximum Angles
Don´t make your control surfaces travel any further than felt really necessary. The idea is to keep induced drag to a minimum, of course. For example, about 15 ° of up and down should be sufficient for ailerons.
Step 4 Mixing Aileron Over Flap
To keep induced drag to a minimum (in theory), proceed like this:
+/- 15 °

## Slide 5: 10.2 FAQs: How do I get maximum performance out of my TEK-Vario-equipped model? (Cont´d)
root tip
Step 4 Mixing Aileron Over Flap (Cont´d)
Draw a line to represent one wing.
root tip
flap
aileron
Mark the middle of the flap and the aileron lengthwise.
*
*
Sketch flap and aileron.

## Slide 6: 10.2 FAQs: How do I get maximum performance out of my TEK-Vario-equipped model? (Cont´d)
Measure from 1(root) to 2 (flap middle) and 1 to 3 (aileron middle):
root tip
*
*
1 60 cm 2 180 cm 3
The ratio between these values equals the ideal travel ratio between the maximum travels of aileron and flap: 60 : 180 = 1 : 3 -> ~ 33 %
The max. travel of the flap is 33% of the max. travel of the aileron.
This is only a point to start from. Test flights will show how well it works with your model. Adjust, if it doesn´t suit you.
Step 4 Mixing Aileron Over Flap (Cont´d)

## Slide 7: 10.2 FAQs: How do I get maximum performance out of my TEK-Vario-equipped model?
Step 5 Adverse Yaw
By tradition, most model pilots simply reduce downward travel of the ailerons to overcome adverse yaw. Physics tells us that there is a better way of dealing with adverse yaw:
You must be familiar with adverse yaw and know what causes it.

## Slide 8: 10.2 FAQs: How do I get maximum performance out of my TEK-Vario-equipped model?
Step 5 Adverse Yaw (Cont´d)
Mix aileron over rudder. When banking to the right, your rudder must travel to the right as well, of course. It is okay to mix up to (or even beyond) 80 % of rudder to the ailerons.
Please be aware, that adverse yaw increases when speed decreases. Therefore, you have to adjust your mixer percentage
according to the standard speed of each flight mode.
During test flights, let a helper keep an eye on speed and ask him to read it out while your are flying and watching your glider.
Try to maintain standard speed throughout your test.

## Slide 9
10.2 FAQs: How do I get maximum performance out of my TEK-Vario-equipped model?
Step 5 Adverse Yaw (Cont´d)
Fly straight away from you.
Repeatedly and fluently put in quite some aileron to initiate fairly fast banks (up to about 30°) to either side in turns.
Repeatedly and fluently put in quite some aileron to initiate fairly fast banks (up to about 30°) to either side in turns. If the tail of the model keeps swinging to either side, you have to put in more rudder. Finally, your model should bank without rotating around the vertical axis. If about 80% rudder doesn´t prevent your model from swiveling around the vertical axis, time has come to reduce downward travel of your ailerons (and maybe your flaps, too).
30°
30°

## Slide 10
10.2 FAQs: How do I get maximum performance out of my TEK-Vario-equipped model?
Step 5 Adverse Yaw (Cont´d)
If the tail of the model keeps swinging to either side, you have to increase rudder.
Finally, your model should bank without rotating around the vertical axis. If about 80% rudder doesn´t prevent your model from swiveling around the vertical axis, time has come to reduce downward travel of your ailerons (and maybe your flaps, too).
By the way: As soon as the whole model starts to tumble from one side to the other, there is too much rudder.

## Slide 11
10.2 FAQs: How do I get maximum performance out of my TEK-Vario-equipped model?
Step 6 Flap Snap
Use flap snap.
Step 7 Centre Of Gravity
Don´t put your centre of gravity too far back. We always fly in fairly bumpy air. So you had better set up your model in a way that it stays on its track rather than being pushed off track by every tiny bubble.
Step 8 Performance Of TEK-Vario
Once your model flies well, time has come to check how well your TEK-Vario performs as a part of your system. -> Simply grasp for Part IV.