## Slide 1: Towards a Better Understanding Of the TEK-Vario Part I

## Slide 2
The other day at the flying field…
„My model is flying well and my conventional vario is beeping happily. Why should I bother using a TEK-Vario instead?“

## Slide 3
If you can´t be bothered: Stop reading here. You´d better go flying.
The other day at the flying field…
„My model is flying well and my conventional vario is beeping happily. Why should I bother using a TEK-Vario instead?“

## Slide 4
If you can´t be bothered: Stop reading here. You´d better go flying.
The other day at the flying field…
„My model is flying well and my conventional vario is beeping happily. Why should I bother using a TEK-Vario instead?“
If you want to acquire knowledge and use this knowledge to improve your skills: Welcome! Your are the one we readily sacrifice our spare time for. We do hope you will enjoy reading on!
Andrej Vrecer, Philip Kolb, Michael Rogg, Neresheim, March 2025

## Slide 5: A TEK-VARIO* is a vario with:
TOTAL
ENERGY
K/COMPENSATION
* Please note: For various reasons, the author decided to use the German term and qoute it throughout.

## Slide 6: A TEK-VARIO is a vario with:
TOTAL
ENERGY
K/COMPENSATION
potential energy (Epot)
kinetic energy (Ekin)
As for energy, we will have to deal with:

## Slide 7: A TEK-VARIO is a vario with:
TOTAL
ENERGY
K/COMPENSATION
Let´s find out what
all these terms
mean in detail.
potential energy (Epot)
kinetic energy (Ekin)

## Slide 8: 1 Air Pressure and Height
The higher you get in the atmosphere, the less air molecules there are.

## Slide 9: 1 Air Pressure and Height
height 0 m
height 100 m
more air molecules -> higher air pressure
less air molecules -> lower air pressure
If height increase is 8 m,
air pressure decreases
by 1 mbar. (0-5000 m ASL)

## Slide 10: 1.1 Static/Ambient Air Pressure
What is “static“ air pressure?
height 100 m
height 0 m
higher static air pressure
lower static air pressure

## Slide 11: 1.1 Static/Ambient Air Pressure
What is “static“ air pressure?
Here “static“ means:
“still“, “not moving“
height 100 m
height 0 m
higher static air pressure
lower static air pressure

## Slide 12: 1.1 Static/Ambient Air Pressure
What is “static“ air pressure?
“Static“ air pressure means the force which not moving air exerts on its surrounding.
height 100 m
height 0 m
higher static air pressure
lower static air pressure

## Slide 13
A conventional vario simply measures
“static air pressure“, usually called “ambient pressure“.
height 100 m
height 0 m
higher static air pressure
lower static air pressure
1.1 Static/Ambient Air Pressure

## Slide 14
height 100 m
height 0 m
higher static air pressure
lower static air pressure
A vario in its glider is taken to different heights. There it measures the prevailing
ambient pressure.
A conventional vario indicates changes in ambient pressure either as a “climb“ or as a “descent“.
1.2 Static/Ambient Air Pressure and Conventional Vario

## Slide 15
Whenever the glider sinks, ambient pressure increases. You can hear a permanent, dark sound.
Whenever the glider climbs, ambient pressure decreases. You can hear a bright sound at intervals.
height 100 m
height 0 m
higher static air pressure
lower static air pressure
1.2 Static/Ambient Air Pressure and Conventional Vario

## Slide 16
Are you familiar with the following terms now?
Air molecules, height, static pressure, ambient pressure, vario, climb, descent, dark and permanent sound, bright sound at intervals
Then let´s go on to the next topic…
1.2 Static/Ambient Air Pressure and Conventional Vario

## Slide 17: 2 What is Potential Energy?
LAE-
ENER-
GIE
Please remember this basic physical law:
We never “lose“ or “use up“ energy.
We just TRANSFORM energy.
So let´s play “Transformers“ from now on .

## Slide 18: 2 What is Potential Energy?
height 0 m
height 100 m
height 50 m
At a height of 0 m, the
potential energy
of this car is “0“.

## Slide 19: 2 What is Potential Energy?
height 0 m
height 100 m
LAE-
ENER-
GIE
height 50 m
Now this man wants to push his car uphill to a height of
50 m. To be able to do so, he needs a certain
amount of muscle energy. He draws his energy from a…

## Slide 20: 2 What is Potential Energy?
height 0 m
height 100 m
LAE-
ENER-
GIE
height 50 m

## Slide 21: 2 What is Potential Energy?
height 0 m
height 100 m
LAE-
ENER-
GIE
height 50 m
As he pushes the car uphill, the muscle energy of the man
is gradually transformed into potential energy of the car.

## Slide 22: 2 What is Potential Energy?
LAE-
ENER-
GIE
height 0 m
height 100 m
height 50 m
At a height of 50 m, the complete muscle energy of the man has been transformed into potential energy of the car. Now the car has the potential energy of “1 sausage“.

## Slide 23: 2 What is Potential Energy?
height 0 m
height 100 m
height 50 m
This potential energy let´s the car roll down the slope.
When the car comes to a standstill at a height of 0 m,
The “sausage“/potential energy is “0“ again.
Halfway down the slope, only “half a sausage“ of energy is left.

## Slide 24: 2 What is Potential Energy?
height 0 m
height 100 m
height 50 m
Guess what!

## Slide 25: 2 What is Potential Energy?
height 0 m
height 100 m
How many “sausage units“ of energy does the man need to push his car up to a height of 100 m?
height 50 m
?

## Slide 26: 2 What is Potential Energy?
height 0 m
height 100 m
LAE-
ENER-
GIE
height 50 m
Yes, indeed:
2 “sausage units of energy“
will do the trick.

## Slide 27: 2 What is Potential Energy?
height 0 m
LAE-
ENER-
GIE

## Slide 28: 2 What is Potential Energy?
LAE-
ENER-
GIE
The same is true for gliders, of course.

## Slide 29: 2 What is Potential Energy?
LAE-
ENER-
GIE
Epot
The rule is:
Twice the height
equals twice the potential energy.

## Slide 30: 3 Your Conventional Vario and Potential Energy
Now let´s combine what we have discussed so far.

## Slide 31: 3 Your Conventional Vario and Potential Energy
height 100 m
height 0 m
higher static air pressure
lower static air pressure
Epot
Although simply measuring ambient air pressure, our conventional vario indicates the potential energy
of our glider.

## Slide 32: 3 Your Conventional Vario and Potential Energy
Epot
Ambient air pressure and potential energy increase or decrease linearly.

## Slide 33: 4 A Closer Look at Different Inflight Situations
 | climb | descent | Vario
1 | Long and steady (initial) climb | Long and steady (final) descent | 
2 | Short climb by pulling the elevator | Short descent by pushing the elevator | 
3 | Phugoid | Phugoid | 
4 | Flight mode change (speed -> thermal) | Flight mode change (thermal -> speed) | 
5 | Transition from a banked turn into straight and level flight | Transition from straight and level flight into a banked turn | 
6 | Transition from falling air into rising air | Transition from rising air into falling air | 
7 | Flying upwind, hit by an oncoming gust | Flying downwind, hit by a gust from the rear | 
8 |  | Sinking in falling air at a rate bigger than the glider´s sink rate. | 
9 |  | Sinking in neutral air at the glider´s sink rate | 
10 |  | Climbing in a thermal, yet still sinking a bit (sink rate of the glider > thermal) | 
11 | Real climb in a thermal (thermal > sink rate) |  | 

## Slide 34: 4 A Closer Look at Different Inflight Situations
Does our conventional vario indicate all the resulting
climbs and descents?

## Slide 35: 4 A Closer Look at Different Inflight Situations
 | climb | descent | Vario
1 | Long and steady (initial) climb | Long and steady (final) descent | ü
2 | Short climb by pulling the elevator | Short descent by pushing the elevator | ü
3 | Phugoid | Phugoid | ü
4 | Flight mode change (speed -> thermal) | Flight mode change (thermal -> speed) | ü
5 | Transition from a banked turn into straight and level flight | Transition from straight and level flight into a banked turn | ü
6 | Transition from falling air into rising air | Transition from rising air into falling air | ü
7 | Flying upwind, hit by an oncoming gust | Flying downwind, hit by a gust from the rear | ü
8 |  | Sinking in falling air at a rate bigger than the glider´s sink rate. | ü
9 |  | Sinking in neutral air at the glider´s sink rate | ü
10 |  | Climbing in a thermal, yet still sinking a bit (sink rate of the glider > thermal) | ü
11 | Real climb in a thermal (thermal > sink rate) |  | ü
Yes!

## Slide 36: 4 A Closer Look at Different Inflight Situations
Is this what the pilot needs?

## Slide 37: 4 A Closer Look at Different Inflight Situations
 | climb | descent | Vario
1 | Long and steady (initial) climb | Long and steady (final) descent | ü
2 | Short climb by pulling the elevator | Short descent by pushing the elevator | ü
3 | Phugoid | Phugoid | ü
4 | Flight mode change (speed -> thermal) | Flight mode change (thermal -> speed) | ü
5 | Transition from a banked turn into straight and level flight | Transition from straight and level flight into a banked turn | ü
6 | Transition from falling air into rising air | Transition from rising air into falling air | ü
7 | Flying upwind, hit by an oncoming gust | Flying downwind, hit by a gust from the rear | ü
8 |  | Sinking in falling air at a rate bigger than the glider´s sink rate. | ü
9 |  | Sinking in neutral air at the glider´s sink rate | ü
10 |  | Climbing in a thermal, yet still sinking a bit (sink rate of the glider > thermal) | ü
11 | Real climb in a thermal (thermal > sink rate) |  | ü
No!

## Slide 38: 4 A Closer Look at Different Inflight Situations
 | climb | descent | Vario
2 | Short climb by pulling the elevator | Short descent by pushing the elevator | ü
3 | Phugoid | Phugoid | ü
4 | Flight mode change (speed -> thermal) | Flight mode change (thermal -> speed) | ü
5 | Transition from a banked turn into straight and level flight | Transition from straight and level flight into a banked turn | ü
6 | Transition from falling air into rising air | Transition from rising air into falling air | ü
7 | Flying upwind, hit by an oncoming gust | Flying downwind, hit by a gust from the rear | ü
What do situations 2-7 have in common?

## Slide 39: 4 A Closer Look at Different Inflight Situations
In every single one of these situations, the glider changes its speed.
 | climb | descent | Vario
2 | Short climb by pulling the elevator | Short descent by pushing the elevator | ü
3 | Phugoid | Phugoid | ü
4 | Flight mode change (speed -> thermal) | Flight mode change (thermal -> speed) | ü
5 | Transition from a banked turn into straight and level flight | Transition from straight and level flight into a banked turn | ü
6 | Transition from falling air into rising air | Transition from rising air into falling air | ü
7 | Flying upwind, hit by an oncoming gust | Flying downwind, hit by a gust from the rear | ü

## Slide 40: 4 A Closer Look at Different Inflight Situations
So what´s the challenge?

## Slide 41: 4 A Closer Look at Different Inflight Situations
We have to improve our vario.
Our future vario…
must not
indicate altitude changes brought on by speed changes
and vice-versa.

## Slide 42: 5 Quick Check
Do you have a clear understanding of potential energy?
Do you have a clear understanding of how a conventional
vario measures it and what it indicates?
Do you have a clear understanding of “what is wrong“ with
a vario that only measures changes in height?
Then let´s take the next hurdle.

## Slide 43: 6 A Closer Look at Kinetic Energy
“Kinetic energy“ is the term for energy that is in moving things.
We already know how potential energy changes with height.
Now let´s find out, how kinetic energy changes with speed.
10 km/h
Let´s say, our candidate transforms 1 “sausage unit“ of energy into
kinetic energy in order to accelerate his car to a speed of 10 km/h.

## Slide 44: 6 A Closer Look at Kinetic Energy
10 km/h
How many units of “sausage energy“ does he need to double the speed?
20 km/h
?

## Slide 45: 6 A Closer Look at Kinetic Energy
10 km/h
20 km/h
Really?
Yes, indeed.

## Slide 46: 6 A Closer Look at Kinetic Energy
It´s because:
Whenever we deal with
kinetic energy, we deal
with squares.
Chart: y = x²

## Slide 47: 6 A Closer Look at Kinetic Energy
Are you ready for
the next step?
Chart: y = x²
Please don´t forget:

## Slide 48: 7 Total Energy
potential energy + kinetic energy
= total energy
Chart: y = x²

## Slide 49: 7 Total Energy
If a glider pitches down, it picks up speed,…
total energy stays the same.
(Neglecting energy loss due to drag.)
Chart: y = x²
potential energy is transformed into kinetic energy, yet…

## Slide 50: 7 Total Energy
If a glider pitches up, it loses speed,…
total energy stays the same.
(Neglecting energy loss due to drag.)
Chart: y = x²
kinetic energy is transformed into potential energy, yet…

## Slide 51: 7 What we have learnt so far…
Potential energy changes …
Kinetic energy changes …
total energy stays the same, kinetic, energy, transformed, in squares, potential, energy, linearly
In this case … energy is … into …, yet …
In this case … energy is … into …, yet …

## Slide 52: 8.1 Energy Compensation
We have to think up some kind of device, that does not indicate a climb or descent, when potential energy is transformed into kinetic energy and vice-versa.
In other words: In these situations our vario must indicate “nothing“ or “0“. We can also say it must “COMPENSATE“ what is going on.

## Slide 53: 8.2 Total Energy Compensation
Now we know exactly, where the TEK-Vario got its name from…
and time has come to change from words to numbers completely:
In fact, the logic behind a TEK-Vario is:
total energy compensation = potential energy + kinetic energy = 0

## Slide 54: 8.3 Total Energy Compensation - Arithmetics
total energy compensation = potential energy + kinetic energy = 0
How can we convert this into numbers completely?
We know, that, if there is potential energy, it always is of positive value. (Otherwise the car wouldn´t roll downhill).
Therefore, setting up an arithmetic task, we must replace “potential energy“ by a positive number. Let´s take a “1“.
total energy compensation = potential energy + kinetic energy = 0
1

## Slide 55: 8.3 Total Energy Compensation - Arithmetics
How can we convert this into numbers completely?
We know, that, if there is potential energy, it always is of positive value. (Otherwise the car wouldn´t roll downhill).
Therefore, setting up an arithmetic task, we must replace “potential energy“ by a positive number. Let´s take a “1“.
total energy compensation = potential energy + kinetic energy = 0
What´s the missing number
to keep this task true?
?
total energy compensation = potential energy + kinetic energy = 0
1

## Slide 56: 8.3 Total Energy Compensation - Arithmetics
How can we convert this into numbers completely?
We know, that, if there is potential energy, it always is of positive value. (Otherwise the car wouldn´t roll downhill).
Therefore, setting up an arithmetic task, we must replace “potential energy“ by a positive number. Let´s take a “1“.
total energy compensation = potential energy + kinetic energy = 0
total energy = potential energy + kinetic energy = 0
Yes, it´s a negative number “1“
-1
1

## Slide 57: 8.4 Total Energy Compensation - Arithmetics + Reality
total energy compensation = 1 + -1 = 0
The logic involved here makes it crystal clear what kind of device we must look for:
The missing device must deliver exactly the opposite value of our conventional vario.

## Slide 58: 8.5 Total Energy Compensation - Summing Up
Let´s sum up:
Potential energy and kinetic energy are quite different by nature and therefore not easy to match.
In order to improve a conventional vario, we have to add a system that delivers exactly the opposite value of our conventional vario. What is more, this must happen at any time and in a system, where potential energy and kinetic keep changing and interacting rapidly and throughout.
For sure a heap of mind boggling problems. Nevertheless, already decades ago engineers found a brilliant solution…
Curious to know? Just start reading Part II!